MACFLO SLIDE VALVE

PVC Gate Valve

Please turn over page for Spec Sheet Description: Size: 1 1/4’’-6’’(DN32-DN150) Standard: DIN,ANSI,BS Material: UPVC Working Pressure: 0.35mpa Widely used in effluent applications.

Materials of Construction

No. Parts Material 1 Faucet UPVC 2 Valve Gate PP, 1Cr13 3 Seat EPDM,NBR 4 Bolt A2 5 Stem 1Cr13 6 Body UPVC 7 Cap UPVC 8 O-Ring EPDM,NBR 9 Bushing UPVC 10 Key UPVC 11 Handle ABS,ZL106

Dimension

Size A B DN Φ L H PN mm(in) (Mpa) 1 1/4'' 143 115 32 40 68 57 0.35 1 1/2'' 170 136 40 50 100 74 0.35 2'' 207 163 50 63 108 86 0.35 2 1/2'' 240 190 65 75 125 104 0.35 3'' 305 222 80 90 128 150 0.35 4'' 350 260 100 110 132 170 0.35 6'' 505 380 150 160 172 242 0.35